## Slide 1: DOG Cube Code
Documentation

## Slide 2: Overview
This code is designed to control the entire DOG setup (Delivery On G-line, colloquially known as the Cube).
This involves interfacing with the Elveflow (gas flow and sheath flow control), pumps (sample/buffer flow control), valves (liquid path control), and SPEC (x-ray control and detector saving), as well as the local file system on the computer (config reading and logging)
Elveflow
Pump
Valves
SPEC
Local file system
GUI Code

## Slide 3: General usage
Start up the software
  Create the GUI
  Load the config (local file system)
  Start the logging (local file system)
  Connect to Elveflow and start up a thread to handle all Elveflow communication
  Connect to spec
Start microcontroller connection (pumps and valves)
Start sheath flow (Elveflow) and automatically graph
Elveflow
Pump
Valves
SPEC
Local file system

## Slide 4: General usage
Press Auto Run
  Create a file name (spec)
  Double-check the Elveflow flowrates
  Start running everything, which involves switching valves, starting and stopping the pumps, telling spec to actually take scans, and graphing Elveflow results to the main page
  Clean everything, which again involves valves and pumps
Purge sheath if necessary (Elveflow and valves)
Elveflow
Pump
Valves
SPEC
Local file system

## Slide 5: General usage
Shutdown
  Close connection to Elveflow (stop the sheath), spec, pump, and valve and the logging file (local file system)
Elveflow
Pumps + Valves
SPEC
Local file system

## Slide 6: Threads
There are a couple threads that we need to be careful of to manage them. Crashing any of them except the main thread will not throw an error and instead will just make the whole program, so this is very hard to debug!
  Main thread (the GUI runs here)
  Elveflow thread (queries the Elveflow every half second or so)
  Graph thread (updates the graph on the Elveflow tab periodically)
    Second graph on front page (?)
  Run queue (sends commands and spin-waits for responses from the pumps and the valves)
  Manual instrument thread (send manual commands to the pumps/valves)
  Spec thread (?)
  State diagram thread (?)

## Slide 7: Bugs
Initialize Sheath currently does not stop until it receives confirmation that it got to the right level—TODO: be allowed to cancel
Something going wrong with the Elveflow if you leave it running for too long